## Slide 1: Lecture 1. Computer Architecture & Design Overview (1)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: About Prerequisite – What to Submit?
If you have 180D in your admission letter
  You then need to submit your transcript with 180D highlighted
  You cannot take this course before finishing 180D
If you do not have 180D in your admission letter
  You then need to submit your admission letter

## Slide 3: Abstraction of Computers
CMPE
CS/SE
EE/Phys
Software/Applications
Processor
Operating System
Digital Design
Circuit Design
ISA
Firmware
Datapath & Control
Compiler
Registers
Cache
Memory
HDD/SSD
CMPE200
Semiconductor physics

## Slide 4: The Software’s Point of View
Application software
  Written in high-level language
System software
  Compiler: translates HLL code to machine code
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
Hardware
  Processor, memory, I/O controllers, …

## Slide 5: The Codes’ Point of View
High-level language
  Abstraction Level closer to problem domain
  Provides for productivity and portability
Assembly language
  Textual representation of instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data

## Slide 6: Hardware’s Point of View
Computer Organization:
Nowadays DRAM

## Slide 7: Your Thoughts
Try to conclude with as few words as possible:
Computer Organization vs. Computer Architecture
– What is the key difference?
Connection vs. interface

## Slide 8: Hardware Examples
Figures from http://www.techinsights.com/teardown.com/apple-iphone-6/
Processor
Main memory
(SDRAM)

## Slide 9: Hardware Examples
Figures from http://www.techinsights.com/teardown.com/apple-iphone-6/
Storage
(NAND Flash)
Input/output device
(touch screen)

## Slide 10: Hardware Examples
Figures from http://www.anandtech.com/show/8562/chipworks-a8
What is the advantage of having them in the same package?

## Slide 11: Electronic Components’ Point of view
Transistors
  3-terminal device
  Gate input: the control input; its voltage determines whether current can flow
  Source & Drain: terminals that current flows from/to
Many transistors can be fabricated on one piece of silicon (i.e. an integrated chip, IC)
Transistor is ‘on’
Transistor is ‘off’
Gate +5V
Source
Drain
-
-
-
-
-
-
High voltage at gate allows current to flow between source and drain
Gate 0V
Drain
-
Low voltage at gate prevents current from flowing between drain and source
-
Silicon
Silicon
Source
Actual silicon wafer is quite small but can contain several billion transistors
Silicon wafer is then packaged to form the chips we are familiar with
Integrated Circuit
More transistors = faster core?

## Slide 12: Moore’s Law (1965)
“The number of transistors per square inch on integrated circuits had doubled every year since the integrated circuit was invented and this trend would continue for the foreseeable future.”
-- Gordon E. Moore, “Cramming More Components onto Integrated Circuits,” Electronics, pp. 114–117, April 19, 1965.
In 1975, he recalibrated it to every two years.
Later, it is recalibrated again to 18 months, as is widely known as Moore’s Law.

## Slide 13: Moore’s Law (1965)
The law has been preserved over four decades..

## Slide 14: What Does It Enable?
Applications that were impossible to run on the computers before
  3D games, Augmented reality, Virtual reality, Deep learning…

## Slide 15: Moore’s Law (1965)
Will it last forever?
Dead?

## Slide 16: Current Trend of Computer Systems
Multi- or Many-core Processors
  - Embedding multiple cores in one CPU
Complex microarchitecture
  - Out-of-order execution, branch predictor, memory prefetcher, etc..
Accelerators
  - GPUs, FPGAs, etc..
  - Application specific designs
Novel architectures
  - Dark silicon, 3D-stacking, neuromorphic computing, quantum, etc..

## Slide 17: Metrics: How Do We Evaluate a System?
Performance (speed)
  Response time (Latency):
    How long it takes to do a task
  Throughput :
    Total work done per unit time
Power efficiency
  How much power it consumes to do a task
Cost

## Slide 18: What Determines Performance?
Algorithm
  Determines number of operations executed
Programming language, compiler, architecture
  Determine number of machine instructions executed per operation
Processor and memory system
  Determine how fast instructions are executed
I/O system (including OS)
  Determines how fast I/O operations are executed

## Slide 19: Relative Performance
Define Performance = 1/Execution Time
“X is n times faster than Y”
Example: time taken to run a program -- 10s on a computer A, 15s on computer B
Execution TimeB / Execution TimeA = 15s / 10s = 1.5
A is 1.5 times faster than B.

## Slide 20: Measuring Execution Time
Elapsed time
  Total response time, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job on CPU
    Discounts I/O time, other jobs’ shares
  Estimating CPU time is relatively easy based on the number of lines of code and processing speed of the CPU

## Slide 21: Conclusion Time
Why do we need multi-core processors to keep the Moore’s Law alive?
How do we evaluate a system?
Adding transistors no longer works
Performance
Power efficiency
Cost

## Slide 22: Conclusion Time
Why do we use CPU time to measure the performance?
Avoid influences