## Slide 1: Lecture 1. Computer Architecture & Design Overview
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Abstraction of Computers
CMPE
CS/SE
EE/Phys
Software/Applications
Processor
Operating System
Digital Design
Circuit Design
ISA
Firmware
Datapath & Control
Compiler
Registers
Cache
Memory
HDD/SSD
CMPE140
Semiconductor physics

## Slide 3: The Software’s Point of View
Application software
  Written in high-level language
System software
  Compiler: translates HLL code to machine code
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
Hardware
  Processor, memory, I/O controllers, …

## Slide 4: The Codes’ Point of View
High-level language
  Abstraction Level closer to problem domain
  Provides for productivity and portability
Assembly language
  Textual representation of instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data

## Slide 5: Hardware’s Point of View
Computer Organization:
Nowadays DRAM

## Slide 6: Your Thoughts
Try to conclude with as few words as possible:
Computer Organization vs. Computer Architecture
– What is the key difference?

## Slide 7: Hardware Examples
Figures from http://www.techinsights.com/teardown.com/apple-iphone-6/
Processor
Main memory
(SDRAM)

## Slide 8: Hardware Examples
Figures from http://www.techinsights.com/teardown.com/apple-iphone-6/
Storage
(NAND Flash)
Input/output device
(touch screen)

## Slide 9: Hardware Examples
Figures from http://www.anandtech.com/show/8562/chipworks-a8
What is the advantage of having them in the same package?

## Slide 10: Electronic Components’ Point of view
Transistors
  3-terminal device
  Gate input: the control input; its voltage determines whether current can flow
  Source & Drain: terminals that current flows from/to
Many transistors can be fabricated on one piece of silicon (i.e. an integrated chip, IC)
Transistor is ‘on’
Transistor is ‘off’
Gate +5V
Source
Drain
-
-
-
-
-
-
High voltage at gate allows current to flow between source and drain
Gate 0V
Drain
-
Low voltage at gate prevents current from flowing between drain and source
-
Silicon
Silicon
Source
Actual silicon wafer is quite small but can contain several billion transistors
Silicon wafer is then packaged to form the chips we are familiar with
Integrated Circuit

## Slide 11: Moore’s Law (1965)
“The number of transistors per square inch on integrated circuits had doubled every year since the integrated circuit was invented and this trend would continue for the foreseeable future.”
-- Gordon E. Moore, “Cramming More Components onto Integrated Circuits,” Electronics, pp. 114–117, April 19, 1965.
In 1975, he recalibrated it to every two years.
Later, it is recalibrated again to 18 months, as is widely known as Moore’s Law.

## Slide 12: Moore’s Law (1965)
The law has been preserved over four decades..

## Slide 13: What Does It Enable?
Applications that were impossible to run on the computers before
  3D games, Augmented reality, Virtual reality, Deep learning…

## Slide 14: Moore’s Law (1965)
Will it last forever?
Dead?

## Slide 15: Current Trend of Computer Systems
Multi- or Many-core Processors
  - Embedding multiple cores in one CPU
Complex microarchitecture
  - Out-of-order execution, branch predictor, memory prefetcher, etc..
Accelerators
  - GPUs, FPGAs, etc..
  - Application specific designs
Novel architectures
  - Dark silicon, 3D-stacking, neuromorphic computing, quantum, etc..

## Slide 16: Metrics: How Do We Evaluate a System?
Performance (speed)
  Response time (Latency):
    How long it takes to do a task
  Throughput :
    Total work done per unit time
Power efficiency
  How much power it consumes to do a task
Cost

## Slide 17: What Determines Performance?
Algorithm
  Determines number of operations executed
Programming language, compiler, architecture
  Determine number of machine instructions executed per operation
Processor and memory system
  Determine how fast instructions are executed
I/O system (including OS)
  Determines how fast I/O operations are executed

## Slide 18: Relative Performance
Define Performance = 1/Execution Time
“X is n times faster than Y”

## Slide 19: Measuring Execution Time
Elapsed time
  Total response time, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job on CPU
    Discounts I/O time, other jobs’ shares
  Estimating CPU time is relatively easy based on the number of lines of code and processing speed of the CPU

## Slide 20: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Different system components may have different clock rates
Clock (cycles)
Data transfer and computation
Update state
Clock period
Clock period: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (rate): cycles per second
  e.g., 4.0GHz = 4000MHz = 4.0×109Hz
A clock cycle

## Slide 21: CPU Time Estimation
A code line of high-level language program can be translated to one or multiple assembly code lines
CPU processes a piece of machine code for each assembly code line, one by one
Example: Application A has 1000 assembly lines. CPU has 250 ps clock period.
Clock cycles for Application A
= 1000 cycles
CPU time for Application A
= 1000 cycles x 250 ps = 250×10–9s

## Slide 22: CPU Time
CPU Time = Clock Cycles x Clock Period
= Clock Cycles / Clock Frequency

## Slide 23: Instruction Count and CPI
An assembly line is also called one Instruction
In some CPUs, an instruction may take multiple clock cycles
CPU Time equation can be rewritten
Cycles Per Instruction is also called CPI
CPU Time
= Clock Cycles x Clock Period
= Instruction Count x Cycles Per Instruction x Clock Period

## Slide 24: CPI Example
A program takes 33 billion instructions to run
CPU processes instructions at 2 cycles per instruction
Clock speed is 3GHz
What is estimated CPU Time for this program?
CPU Time = Instruction Count x CPI x Clock Period
= 33 x 109 x 2 x 1/(3 x 109)
= 22 seconds

## Slide 25: CPI and Average CPI
In some CPUs, different types of instructions (i.e. integer instruction vs. floating point instruction) may take different number of cycles
CPU Time equation can be rewritten
Average CPI
  = Total Clock Cycles / Total IC
  = / Total IC
CPU Time = Clock Cycles x Clock Period
= x Clock Period
Sum of (IC of each type instruction x CPI of the type)
(IC = instruction count)

## Slide 26: Example: Average CPI
Instruction Type | Integer | Floating point | Branch | Load/ Store
CPI for type | 1 | 2 | 4 | 3
Instruction Count in program A | 50 | 10 | 10 | 10
Instruction Count in program B | 20 | 0 | 10 | 10
Program A: Total Instructions = 80
Clock Cycles = 50×1 + 10×2 + 10×4 + 10x3 = 140
Avg. CPI = 140/80 = 1.75
CPU time (if Clock period = 100 ps)
  = 1.75 x 80 x 100ps = 14000 ps = 14ns

## Slide 27: Power and Performance
In CMOS IC technology
Power = Capacitive load x Voltage2 x Frequency

## Slide 28: Issue with Power Scaling
Increasing core frequency may burn your processor!
  - Almost all energy consumption turns into heat
Cooling is costly
Design more efficient system instead
- Multicore, etc..