## Slide 1: Lecture 3. Processor Microarchitecture and Design (1)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Instruction Processing
CPU
A 32-bit instruction
Decoder
The instruction is
- Opcode: add
- Rs: $4
- Rt: $3
- Rd: $5
Compiled machine code
Return address
*fp
size
sum
numbers[1]
numbers[0]
add*
Value of $4
Value of $3
Calculated result
To be stored to $5
Instruction Processing

## Slide 3: Instruction Execution on CPU
To run a software, CPU
  Fetches instructions from memory in the right order
  Decodes the instruction and Reads the operand values from register file
  Executes the computation by using ALU
  Loads/store data from/to memory
  Writes back the computation results to register file
Instruction Fetch
Decode & Register
Identify opcode & read operands
Execute
Mem
Write Result
Write to
dst register

## Slide 4: Implementing a Single-Cycle CPU
All instructions execute in a single clock cycle
  Instructions to Implement: LW, SW; ADD, SUB, AND, OR, SLT; BEQ
  CPI = 1
Different instructions need different execution times
  i.e. LW needs to access memory vs. ADD does not need to access memory
Single-cycle CPU’s clock cycle period should be set to the longest instruction’s execution time

## Slide 5: Fetch Components
Required operations
  Taking address from PC and reading instruction from memory
  Incrementing PC to point at next instruction
Components
  PC register
  Instruction Memory / Cache
  Adder to increment PC value
I-Cache / I-MEM
Addr.
Data
From PC
Instruction Word
PC
+
A
B
CLK
S
Register
Adder
Memory
/
32
/
32
/
32
/
32
/
32
/
32
/
32

## Slide 6: Fetch Data Path
I-Cache / I-MEM
Addr.
Data
Instruction Word
PC
+
A
B
CLK
S
4
Current PC / Read Address
“Next” PC = PC + 4

## Slide 7: Fetch Data Path
PC value serves as address to instruction memory while also being incremented by 4 using the adder
Instruction word is returned by memory after some delay
New PC value is clocked into PC register at the end of clock cycle
I-Cache / I-MEM
Addr.
Data
Instruction Word
PC
+
A
B
CLK
S
4
Current PC / Read Address
“Next” PC = PC + 4
ADD $3,$1,$2
000000
00001
00010
00000
00011
100000
opcode
rs
rt
shamt
rd
func
Current PC
Current PC + 4

## Slide 8: Decode
What is the instruction and operands?
Decode & Register
Identify opcode & read operands
Execute
Mem
Write Result
Write to
dst register

## Slide 9: Instruction Formats
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store
(I-type)
Branch
(I-type)
opcode
always read
read, except for load
write for R-type and load
sign-extend and add
different ALU instructions

## Slide 10: Decode Components
Register file is a collection of registers
To support R-type instruction,
  4 Input ports : two src register ids, a dst register id and the result value
  2 Output ports : two operand values
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Register File
/
5
/
5
/
5
RegWrite
/
32
/
32
/
32
CLK

## Slide 11: Decode Data Path
5
2
R-type
  Opcode and func. field are decoded to produce control signals
  Three register ids are passed to Register file
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
000000
00001
00010
00000
00011
100000
opcode
rs
rt
shamt
rd
func
Control Signals
Register File
5
1
Value of $1
Value of $2
5
3
Instruction Word
ADD $3,$1,$2
Control Signals for R-type
RegWrite
CLK

## Slide 12: Sign Extension Unit
In a ‘LW’ or ‘SW’ instructions with their base register + offset format, the instruction only contains the offset as a 16-bit value
  Example: LW $4,-8($1)
  Machine Code: 0x8c24fff8
A 16-bit offset must be extended to 32-bits to add to the base register
100011
00001
00100
1111 1111 1111 1000
opcode
rs
rt
offset
Sign Extend
16
32
offset = 0xfff8
0xfffffff8
LW $4,0xfff8($1)

## Slide 13: Decode Data Path
5
4
I-type
  Opcode field is decoded to produce control signals
  Two register ids are passed to Register file
  Offset is sign extended
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
010111
00001
00100
1111 1111 1111 1000
opcode
rs
rt
offset
Control Signals
Register File
5
1
Value of $1
Instruction Word
Sign Extend
16
32
LW $4,0xfff8($1)
RegWrite
CLK

## Slide 14: Execution & Write Result
Let’s execute the instruction!
Execute
Mem
Write Result
Write to
dst register

## Slide 15: Execution Components
ALU is used for
  R-type instructions to operate various arithmetic operations
  LW/SW instructions to operate (base address + offset) to generate the target memory address
  Branch instructions to compare (subtract) the two operand values
Data Memory for LW/SW instructions
Shift-left-2 and another Adder for Branch instructions to calculate new PC value
ALU
/
32
/
32
/
32
ALU Result
Zero
ALU Operation
Data Memory
Read Addr.
Read Data
Write Addr.
Read
Write Data
Write
ALU
Adder
Sum
PC+4 (incremented PC)
Shift Left 2
/
32
/
32
/
32
/
32
/
32
Shift-left-2
Adder
CLK

## Slide 16: Datapath for R-type Instructions
ALU takes inputs from register file and performs the add, sub, and, or, slt, operations
Result is written back to dest. register
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
ALU
Res.
$1 value
$2 value
Sum
1
2
3
Instruc. word
ADD
we_reg
ADD $3,$1,$2
CLK
ALU Operation is determined by a control logic according to Opcode & Funct

## Slide 17: Memory Access Datapath: LW
Operands are read from register file while offset is sign extended
ALU calculates target memory address
Memory access is performed
If LW, read data is written back to register
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
LW $4,0xfff8($1)
$1 value
32
0xffff fff8
Sum
Read Data
1
4
0xfff8
ADD
CLK
CLK

## Slide 18: Memory Access Datapath: SW
Operands are read from register file while offset is sign extended
ALU calculates target memory address
If SW, data is written to the memory
D-Cache /
D-Mem
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
ALU
Res.
Zero
Addr.
Read Data
Write Data
SW $3,0x1a($1)
32
0x0000001a
$1 value
Sum
1
3
$3 value
Write Data
0x001a
ADD
we_dm
CLK
CLK

## Slide 19: Branch Datapath: BEQ
ALU for comparison (examine ‘zero’ output)
Sign extension unit for branch offset
Adder to add PC and offset
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
ALU
Res.
Zero
BEQ $1,$2,offset
$1 value
$2 value
SUB
Sign Extend
extended word offset
Adder
Sum
PC+4 (incremented PC)
Shift Left 2
Branch Target Address to PC
word offset
ZERO
1
2
PC
if(zero == 1)
CLK

## Slide 20: Single-Cycle Datapath
R-type
Memory Operations
Branch
20
Decode to Writeback paths are different for different instruction types
 Can we merge them?

## Slide 21: alu_src Mux
Mux controlling second input to ALU
  ALU instruction provides Read Register 2 data to the 2nd input of ALU
  LW/SW uses 2nd input of ALU as an offset to form effective address
Memory operation
R-type
alu_src | MUX Output
0 | Register output 2
1 | Sign extended data
D

## Slide 22: dm2reg Mux
Mux controlling writeback value to register file
  ALU instructions use the result of the ALU
  LW uses the read data from data memory
R-type
Memory operation
dm2reg | MUX Output
0 | ALU output
1 | Data memory Output
D

## Slide 23: reg_dst Mux
Different destination register ID fields for ALU and LW instructions
R-type
Memory operation
instruction[20-16]
instruction[15-11]
reg_dst | MUX Output
0 | instruction [20-16]
1 | instruction [15-11]

## Slide 24: pc_src Mux
Next instruction can either be at the next sequential address (PC+4) or the branch target address (PC+offset)
Normal
Branch
pc_src | MUX Output
0 | PC+4
1 | Branch target address

## Slide 25: Single-cycle CPU Datapath
25
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
32
Sum
Read Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
pc_src
0
1
[25-21]
[20-16]
[15-11]
[15-0]
CLK
we_reg
Taken branch or not
How to decide pc_src?
CLK
reg_dst
alu_src
alu_ctrl
dm2reg
we_dm

## Slide 26: Single-cycle CPU Datapath
26
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
32
Sum
Read Data
0
1
alu_src
0
1
dm2reg
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
0
1
reg_dst
[25-21]
[20-16]
[15-11]
[15-0]
Branch
we_dm
we_reg
alu_ctrl
CLK
CLK

## Slide 27: Single-cycle CPU Datapath
27
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
32
Sum
Read Data
0
1
alu_src
0
1
dm2reg
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
0
1
reg_dst
[25-21]
[20-16]
[15-11]
[15-0]
branch
Control
we_dm
we_reg
[31-26], [5-0]
The Opcode and funct are used for generating selector values
CLK
CLK
alu_ctrl
opcode & funct

## Slide 28: Single-cycle CPU Control Unit
The control unit is a combinational decoder for the single-cycle CPU
The CU contains
  A main decoder for Opcode
  An ALU decoder for Funct
Control Unit
Main Decoder
Opcode5:0
ALU
Decoder
Funct5:0
dm2reg
we_dm
branch
alu_src
reg_dst
we_reg
alu_ctrl
alu_op

## Slide 29: ALU Usage
Load/Store:
  Memory address = Base address + offset  add
Branch:
  Branch if two values are equal/not equal  subtract
R-type:
  Opcode & Funct field together indicates an ALU operation
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
R-type
These three instruction types can be distinguished by Opcode

## Slide 30: Single-cycle CPU Control Unit
Main Decoder is used to generate instruction type indicator & mux control
  To cover 3 types of instructions, we need a 2-bit indicator, alu_op
  alu_op will be the input of ALU Decoder
For R-type instructions, the ALU Decoder will also check the Funct field
Instruction | Opcode | we_reg | reg_dst | alu_src | branch | we_dm | dm2reg | alu_op1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
Input
Output

## Slide 31: ALU Decoder
opcode | alu_op1:0 | Operation | funct | ALU function | alu_ctrl2:0
lw | 00 | load word | XXXXXX | ADD | 010
sw | 00 | store word | XXXXXX | ADD | 010
beq | 01 | branch equal | XXXXXX | SUB | 110
R-type | 10 | ADD | 100000 | ADD | 010
 |  | SUB | 100010 | SUB | 110
 |  | AND | 100100 | AND | 000
 |  | OR | 100101 | OR | 001
 |  | SLT | 101010 | SLT | 111
Input
Input
Output

## Slide 32: So Far…
Our design supports the following instructions
  Memory Reference Instructions:
    LW, SW
  Arithmetic and Logic Instructions:
    ADD, SUB, AND, OR, SLT
  Branch and Jump Instructions:
    BEQ
How to extend the design to support more MIPS instructions?

## Slide 33: Extension to Support addi
33
No need to extend the current datapath
Need to extend the control unit, specifically only the Main Decoder

## Slide 34: Main Decoder for addi
Instruction | Opcode | we_reg | reg_dst | alu_src | branch | we_dm | dm2reg | alu_op1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
addi | 001000 | 1 | 0 | 1 | 0 | 0 | 0 | 00

## Slide 35: Extension to Support j
35
Can we support j with this datapath?
?

## Slide 36: Extension to Support j
36
Both datapath and control unit (main decoder) need to be extended

## Slide 37: Main Decoder for j
Instruction | Opcode | we_reg | reg_dst | alu_src | branch | we_dm | dm2reg | alu_op1:0 | Jump
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01 | 0
addi | 001000 | 1 | 0 | 1 | 0 | 0 | 0 | 00 | 0
j | 000010 | 0 | X | X | X | 0 | X | XX | 1

## Slide 38: Datapath of LW instruction
There are parallel paths.
The longest path (critical path) decides the execution time of the instruction.

## Slide 39: Single-Cycle CPU Performance Analysis
Critical path for LW = Tpcq_PC + Ti-mem + TRFread + TALU + Td-mem + TMUX + TRFwrite
= (30 + 250 + 150 + 200 + 250 + 25 + 20) ps
= 925 ps
Function Unit | Parameter | Delay (ps)
Register clock-to-Q | Tpcq_PC | 30
MUX | TMUX | 25
Sign-extend | Ts_ext | 25
ALU | TALU | 200
Mem read | Tmem | 250
Register file read | TRFread | 150
Register file write | TRFwrite | 20

## Slide 40: Single-Cycle CPU Performance Analysis
The longest instruction’s execution time is 925 ps.
If we run 100 billion instructions, what is the total execution time?
The clock cycle period should be set to 925 ps
CPU time = # instructions x CPI x cycle period
= 100 x 109 x 1 x 925 x 10-12
= 92.5 seconds

## Slide 41: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Violates design principle
  Making the common case fast
  More arithmetic operations than memory operations
Most modern CPUs use multi-cycle processors
  Each instruction takes multiple cycles
  Multiple instructions can execute concurrently (parallelism  pipelining)

## Slide 42: Pipelining Analogy
Laundry tasks
  Place one dirty load of clothes in the washer
  Place the wet load in the dryer
  Place the dry load on a table and fold
  Ask your roommate to put the clothes away

## Slide 43: Pipelining Analogy
Lots of dirty clothes -- need to wash them over four separate loads
Assume each task takes 30 minutes
Inefficient!

## Slide 44: Pipelining Analogy
You can start the next load as soon as the washer finishes washing the previous load
Saved 4.5 hours

## Slide 45: Pipelining Analogy
We can parallelize the single-cycle CPU tasks in a similar way
Pipelined laundry  overlapping execution
Pipelined CPU
clock cycle period = 0.5hrs
Single-cycle CPU
clock cycle period = 2hrs

## Slide 46: MIPS Pipeline
5 steps in one cycle for single-cycle CPU design
  With each step using separate resources
Instruction Fetch
Decode & Register
Identify opcode & read operands
Execute
Mem
Write Result
Write to
dst register
CLK

## Slide 47: MIPS Pipeline
Entire datapath can be broken into five stages
Cycle period is changed to the time taken for a stage
  Shorter clock cycle
  Higher CPI (e.g., CPI = 5 in MIPS)
CLK
Instruction Fetch
Decode & Register
Identify opcode & read operands
Execute
Mem
Write Result
Write to
dst register

## Slide 48: MIPS Pipeline
Entire datapath can be broken into five stages
Cycle period is changed to the time taken for a step
  Shorter clock cycle
  Higher CPI (e.g., CPI = 5 in MIPS)
  System can achieve CPI = 1 by overlapping Multiple Instructions
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
Inst1 | IF | ID | EXE | MEM | WB |  |  |  |  |  | 
Inst2 |  | IF | ID | EXE | MEM | WB |  |  |  |  | 
Inst3 |  |  | IF | ID | EXE | MEM | WB |  |  |  | 
Inst4 |  |  |  | IF | ID | EXE | MEM | WB |  |  | 
Inst5 |  |  |  |  | IF | ID | EXE | MEM | WB |  | 
cc: clock cycle
After initial pipeline filling phase,
we can finish an instruction every cycle
Initial pipeline filling phase

## Slide 49: Pipeline Performance Example
100ps for register IOs (i.e., decode, writeback); 200ps for other stages
What would be the cycle period in single-cycle and pipelined datapath?
What would be the execution time of lw instruction?
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-type | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 50: Pipeline Performance Example
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)
Tc = Longest instruction
Tc = Longest Stage
Tlw = 800ps
Tlw = 1000ps
2 x Tlw = 1600ps
2 x Tlw = 1200ps
…
…

## Slide 51: Basic 5 Stage Pipeline
Same structure as single cycle but now broken into 5 stages
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
32
Sum
Read Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
16
IF
(Instruction Fetch)
ID
(Instruction Decode)
EX
(Execute)
MEM
(Memory Access)
WB
(Writeback)
0
1

## Slide 52: Pipeline Stage Registers
Intermediate results need to be stored to allow stage reuse
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1

## Slide 53: Pipeline Example: LW $t1, 4($s0)
Fetch instr. and increment PC
I-Cache / I-MEM
Addr.
Data
PC
CLK
+
A
B
S
4
0
1
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
Adder
Sum
Shift Left 2
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
ID/EX
EX/MEM
MEM/WB
0
1
IF/ID

## Slide 54: Pipeline Example: LW $t1, 4($s0)
I-Cache / I-MEM
Addr.
Data
PC
CLK
+
A
B
S
4
0
1
IF/ID
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
Adder
Sum
Shift Left 2
EX/MEM
MEM/WB
0
1
Read $s0 values
ID/EX
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
LW $t1,4($s0) machine code

## Slide 55: Pipeline Example: LW $t1, 4($s0)
Calculate memory address
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
MEM/WB
0
1
Offset=0x00000004 / $s0 value
EX/MEM
ID/EX

## Slide 56: Pipeline Example: LW $t1, 4($s0)
Read data from memory
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
0
1
EX/MEM
MEM/WB
Memory Address

## Slide 57: Pipeline Example: LW $t1, 4($s0)
Store data to register file
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
0
1
MEM/WB
Data read from memory

## Slide 58: Pipeline Example: LW $t1, 4($s0)
Store data to register file
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
0
1
MEM/WB
Data read from memory
Is this $t1 (LW’s dest. reg)?

## Slide 59: Revised Datapath
Dest. register number should be stored in the pipeline registers
The dest. register number is passed together with data during writeback
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1

## Slide 60: Pipeline Example: ADD $t4,$t5,$t6
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
ID/EX
EX/MEM
MEM/WB
0
1
Fetch instr. and increment PC
IF/ID

## Slide 61: Pipeline Example: ADD $t4,$t5,$t6
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
EX/MEM
MEM/WB
0
1
Read $t5, $t6 values
ADD $t4,$t5,$t6 machine code
IF/ID
ID/EX

## Slide 62: Pipeline Example: ADD $t4,$t5,$t6
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
MEM/WB
0
1
Calculate $t5 + $t6
EX/MEM
ID/EX
$t4 # / $t6 # / $t6 value / $t5 value

## Slide 63: Pipeline Example: ADD $t4,$t5,$t6
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
0
1
pass through the sum
MEM/WB
EX/MEM
$t4 # / Sum of $t5 + $t6

## Slide 64: Pipeline Example: ADD $t4,$t5,$t6
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
0
1
Store the sum to $t4
$t4 # / Sum of $t5 + $t6
MEM/WB

## Slide 65: Multiple Instructions in 5-Stage Pipeline
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
Fetch
- LW

## Slide 66: Multiple Instructions in 5-Stage Pipeline
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
Fetch
- ADD
Read Operands
- LW
LW $t1,4($s0)

## Slide 67: Multiple Instructions in 5-Stage Pipeline
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
Fetch
- BEQ
Read Operands
- ADD
Calculate Address
- LW
ADD $t4,$t5,$t6
$t1 reg. # / $s0 data / 0x04

## Slide 68: Multiple Instructions in 5-Stage Pipeline
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
Fetch
- Next Instr.
Read Operands
- BEQ
Add Operands
- ADD
Memory Load
- LW
$t4 reg. # / $t5 and $t6 data
BEQ / $a0,$a1 / displacement
$t1 reg #. / $s0 + 4

## Slide 69: Multiple Instructions in 5-Stage Pipeline
Fetch
- Next Instr. + 1
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
Read Operands
- Next Instr.
Calculating Branch PC
Compare Operands - LW
Pass Result
- ADD
Write to $t1
- LW
BEQ / $a0,$a1 vals / disp.
Next instr.
$t1 reg # / Data
$t4 reg # / Sum

## Slide 70: Multiple Instructions in 5-Stage Pipeline
Fetch
- Next Instr. + 2
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
Read Operands
- Next Instr. + 1
Execute
- Next Instr.
If $a0!=$a1,
do nothing - BEQ
Write Result to
Register - ADD
Next instr.
Next instr. + 1
R4 reg # / Sum
Control / Displacement

## Slide 71: Multiple Instructions in 5-Stage Pipeline
Fetch
- Next Instr. + 3
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
Read Operands
- Next Instr. + 2
Execute
- Next Instr. + 1
Mem Access
- Next Instr.
Do Nothing
- BEQ
Next instr. + 1
Next instr. + 2
BEQ – Do nothing
Next instr.

## Slide 72: Pipelined Timing
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF | ID | EXE | MEM | WB |  |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  |  | 
SW |  |  |  | IF | ID | EXE | MEM | WB |  |  | 
AND |  |  |  |  | IF | ID | EXE | MEM | WB |  | 
OR |  |  |  |  |  | IF | ID | EXE | MEM | WB | 
XOR |  |  |  |  |  |  | IF | ID | EXE | MEM | WB
Suppose we execute N instructions using a K stage datapath
Total execution cycle: K+N-1 cycles
  K cycle for 1st inst + (N-1) cycles for remaining insts
  Assume we keep the pipeline full
7 Instrs. =
11 clocks (5 + 7 – 1)

## Slide 73: 5-Stage Pipelined CPU
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
Where do the control signals go?

## Slide 74: Pipelined Control
Using the same control signals as in Single-cycle CPU
Grouped in three pipeline stages
Instruction | EXE stage |  |  | MEM stage |  | WB stage | 
 | alu_op1:0 | reg_dst | alu_src | branch | we_dm | dm2reg | we_reg
R-type | 10 | 1 | 0 | 0 | 0 | 0 | 1
lw | 00 | 0 | 1 | 0 | 0 | 1 | 1
sw | 00 | X | 1 | 0 | 1 | X | 0
beq | 01 | X | 0 | 1 | 0 | X | 0

## Slide 75: Pipelined Control
Control signals are generated in ID stage and used by the following three stages
Pipeline registers are extended to also include control information

## Slide 76: Throughput
Pipeline IPC | N / (N+K-1)
Let n → ∞ (n = infinity) | 1
Throughput (T) = # of instructions executed / time
IPC = Instruction Per Cycle = 1 / CPI
  For a large number of instructions, the IPC of a pipelined processor is 1 instruction per clock cycle
  Only when we keep the pipeline full of instructions
Assume we execute N instructions using a K stage datapath

## Slide 77: Hazards
Any sequence of instructions that prevent full pipeline utilization
  Often causes the pipeline to stall for one or more instructions
Structural Hazards
  HW organization cannot support certain combinations of instructions being overlapped
Data Hazards
  Data dependencies
Control Hazards
  Branches & changes to PC in the pipeline
  If branch is determined to be taken later in the pipeline, flush (delete) the instructions in the pipeline that shouldn’t be executed

## Slide 78: Structural Hazards
Combinations of instructions that cannot be overlapped in the given order due to HW constraints
  Often due to lack of HW resources
Example: A single memory rather than separate I & D Memories
  Structural hazard whenever an instruction needs to perform a data access (i.e. ‘lw’ or ‘sw’)
Memory
ALU
Reg.
File
PC
LW
i+2
i+1
i
Hazard!
78

## Slide 79: Data Hazards
Read-After-Write (RAW)
  A following instruction reads a result from a previous instruction
Write-After-Read (WAR)
Write-After-Write (WAW)
RAW Example
  LW $t1,4($s0)
  ADD $t5,$t1,$t4
Initial Conditions:
$s0 = 0x10010000
$t1 = 0x0
$t4 = 0x24
After execution values should be:
$t5 = 0x0
00000060
12345678
0x10010000
0x10010004
$s0 = 0x10010000
$t1 = 0x60
$t4 = 0x24
$t5 = 0x84

## Slide 80: Data Hazards Example
ALU
Res.
Zero
D-Cache /
D-Mem
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
ID/EX
EX/MEM
MEM/WB
0
1
IF/ID
Fetch LW
00000060
0x10010004
$s0 = 0x10010000
$t1 = 0x0
$t4 = 0x24
$t5 = 0x0

## Slide 81: Data Hazards Example
ALU
Res.
Zero
D-Cache /
D-Mem
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
ID/EX
EX/MEM
MEM/WB
0
1
IF/ID
Fetch ADD
00000060
0x10010004
$s0 = 0x10010000
$t1 = 0x0
$t4 = 0x24
$t5 = 0x0
LW $t1,4($s0)
Decode LW
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16

## Slide 82: Data Hazards Example
Adder
ALU
Res.
Zero
D-Cache /
D-Mem
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Sum
+
A
B
S
4
0
1
ID/EX
EX/MEM
MEM/WB
0
1
IF/ID
Fetch Next instr.
00000060
0x10010004
$s0 = 0x10010000
$t1 = 0x0
$t4 = 0x24
$t5 = 0x0
Decode ADD
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
ADD $t5,$t1,$t4
$t1 reg. # / $s0 data / 0x04
Shift Left 2
Execute LW

## Slide 83: Data Hazards Example
D-Cache /
D-Mem
Adder
ALU
Res.
Zero
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Sum
+
A
B
S
4
0
1
ID/EX
EX/MEM
MEM/WB
0
1
IF/ID
Fetch Next instr. + 1
00000060
0x10010004
$s0 = 0x10010000
$t1 = 0x0
$t4 = 0x24
$t5 = 0x0
Decode Next instr.
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
Shift Left 2
Execute ADD
$t5 reg. # / 0x0 and 0x24
Next instr.
$t1 reg #. / $s0 + 4
Memory LW
ADD uses wrong operand value
because $t1 is not updated by LW yet

## Slide 84: Data Hazards Example
D-Cache /
D-Mem
Adder
ALU
Res.
Zero
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Sum
+
A
B
S
4
0
1
ID/EX
EX/MEM
MEM/WB
0
1
IF/ID
Fetch Next instr. + 2
00000060
0x10010004
$s0 = 0x10010000
$t1 = 0x60
$t4 = 0x24
$t5 = 0x0
Decode Next instr. + 1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
Shift Left 2
Execute Next instr.
Memory ADD
Writeback LW
Next instr.
Next instr. + 1
$t1 reg. # / 0x60
$t5 reg. # / 0x24
It is already too late to use the updated data

## Slide 85: Data Hazards Solutions
Hardware
  Stall the pipeline until the result is written back to the register file
  Use forwarding / bypassing
Compiler
  Reorder Code
Stalling the pipeline:
  All instructions in front of the stalled instruction can continue
  All instructions behind the stalled instruction must also stall
  Stalling inserts “bubbles” / nops (no-operations) into the pipeline
    A “nop” is an actual instruction in the MIPS ISA that does NOTHING

## Slide 86: Pipeline Stall for Data Hazards
Adder
ALU
Res.
Zero
D-Cache /
D-Mem
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Sum
+
A
B
S
4
0
1
ID/EX
EX/MEM
MEM/WB
0
1
IF/ID
Fetch Next instr.
00000060
0x10010004
$s0 = 0x10010000
$t1 = 0x0
$t4 = 0x24
$t5 = 0x0
Decode ADD
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
ADD $t5,$t1,$t4
$t1 reg. # / $s0 data / 0x04
Shift Left 2
Execute LW

## Slide 87: Pipeline Stall for Data Hazards
D-Cache /
D-Mem
Adder
ALU
Res.
Zero
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Sum
+
A
B
S
4
0
1
ID/EX
EX/MEM
MEM/WB
0
1
IF/ID
Fetch Next instr.
00000060
0x10010004
$s0 = 0x10010000
$t1 = 0x0
$t4 = 0x24
$t5 = 0x0
Decode ADD (stalled)
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
ADD $t5,$t1,$t4
Shift Left 2
Memory LW
NOP
$t1 reg #. / $s0 + 4

## Slide 88: Pipeline Stall for Data Hazards
D-Cache /
D-Mem
Adder
ALU
Res.
Zero
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Sum
+
A
B
S
4
0
1
ID/EX
EX/MEM
MEM/WB
0
1
IF/ID
Fetch Next instr.
00000060
0x10010004
$s0 = 0x10010000
$t1 = 0x60
$t4 = 0x24
$t5 = 0x0
Decode ADD (stalled)
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
ADD $t5,$t1,$t4
Shift Left 2
NOP
$t1 reg. # / 0x60
Writeback LW
NOP

## Slide 89: Pipeline Stall for Data Hazards
D-Cache /
D-Mem
Adder
ALU
Res.
Zero
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Sum
+
A
B
S
4
0
1
ID/EX
EX/MEM
MEM/WB
0
1
IF/ID
Fetch Next instr. + 1
00000060
0x10010004
$s0 = 0x10010000
$t1 = 0x60
$t4 = 0x24
$t5 = 0x0
Decode Next instr.
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
Shift Left 2
Execute ADD
$t5 reg. # / 0x60 and 0x24
Next instr.
Now ADD uses correct operand!
NOP
NOP

## Slide 90: Data Hazards Example
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF |  |  |  |  |  |  |  |  |  | 
ADD |  |  |  |  |  |  |  |  |  |  | 
Next instr. |  |  |  |  |  |  |  |  |  |  | 
Next+1 |  |  |  |  |  |  |  |  |  |  | 
Next+2 |  |  |  |  |  |  |  |  |  |  | 
Next+3 |  |  |  |  |  |  |  |  |  |  | 
Next+4 |  |  |  |  |  |  |  |  |  |  | 
Using stalls to handle dependencies

## Slide 91: Data Hazards Example
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF | ID |  |  |  |  |  |  |  |  | 
ADD |  | IF |  |  |  |  |  |  |  |  | 
Next instr. |  |  |  |  |  |  |  |  |  |  | 
Next+1 |  |  |  |  |  |  |  |  |  |  | 
Next+2 |  |  |  |  |  |  |  |  |  |  | 
Next+3 |  |  |  |  |  |  |  |  |  |  | 
Next+4 |  |  |  |  |  |  |  |  |  |  | 
Using stalls to handle dependencies

## Slide 92: Data Hazards Example
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF | ID | EXE |  |  |  |  |  |  |  | 
ADD |  | IF | ID |  |  |  |  |  |  |  | 
Next instr. |  |  | IF |  |  |  |  |  |  |  | 
Next+1 |  |  |  |  |  |  |  |  |  |  | 
Next+2 |  |  |  |  |  |  |  |  |  |  | 
Next+3 |  |  |  |  |  |  |  |  |  |  | 
Next+4 |  |  |  |  |  |  |  |  |  |  | 
Using stalls to handle dependencies

## Slide 93: Data Hazards Example
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF | ID | EXE |  |  |  |  |  |  |  | 
ADD |  | IF | ID |  |  |  |  |  |  |  | 
Next instr. |  |  | IF |  |  |  |  |  |  |  | 
Next+1 |  |  |  |  |  |  |  |  |  |  | 
Next+2 |  |  |  |  |  |  |  |  |  |  | 
Next+3 |  |  |  |  |  |  |  |  |  |  | 
Next+4 |  |  |  |  |  |  |  |  |  |  | 
Hazard
Dependency detected
Using stalls to handle dependencies

## Slide 94: Data Hazards Example
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF | ID | EXE | MEM |  |  |  |  |  |  | 
ADD |  | IF | ID |  |  |  |  |  |  |  | 
Next instr. |  |  | IF |  |  |  |  |  |  |  | 
Next+1 |  |  |  |  |  |  |  |  |  |  | 
Next+2 |  |  |  |  |  |  |  |  |  |  | 
Next+3 |  |  |  |  |  |  |  |  |  |  | 
Next+4 |  |  |  |  |  |  |  |  |  |  | 
nop
nop
Using stalls to handle dependencies
Stays in ID stage

## Slide 95: Data Hazards Example
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF | ID | EXE | MEM | WB |  |  |  |  |  | 
ADD |  | IF | ID |  |  |  |  |  |  |  | 
Next instr. |  |  | IF |  |  |  |  |  |  |  | 
Next+1 |  |  |  |  |  |  |  |  |  |  | 
Next+2 |  |  |  |  |  |  |  |  |  |  | 
Next+3 |  |  |  |  |  |  |  |  |  |  | 
Next+4 |  |  |  |  |  |  |  |  |  |  | 
nop
nop
nop
nop
Using stalls to handle dependencies
Read new value again

## Slide 96: Data Hazards Example
Using stalls to handle dependencies
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF | ID | EXE | MEM | WB |  |  |  |  |  | 
ADD |  | IF | ID |  |  | EXE |  |  |  |  | 
Next instr. |  |  | IF |  |  | ID |  |  |  |  | 
Next+1 |  |  |  |  |  | IF |  |  |  |  | 
Next+2 |  |  |  |  |  |  |  |  |  |  | 
Next+3 |  |  |  |  |  |  |  |  |  |  | 
Next+4 |  |  |  |  |  |  |  |  |  |  | 
nop
nop
nop
nop

## Slide 97: Data Hazards Example
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11 | CC12 | CC13
LW | IF | ID | EXE | MEM | WB |  |  |  |  |  |  |  | 
ADD |  | IF | ID |  |  | EXE | MEM | WB |  |  |  |  | 
Next instr. |  |  | IF |  |  | ID | EXE | MEM | WB |  |  |  | 
Next+1 |  |  |  |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+2 |  |  |  |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+3 |  |  |  |  |  |  |  | IF | ID | EXE | MEM | WB | 
Next+4 |  |  |  |  |  |  |  |  | IF | ID | EXE | MEM | WB
nop
nop
nop
nop
Throughput = 7 insts/13 cycles = 0.53
vs.
Throughput without hazard = 7 insts/11 cycles = 0.63
Using stalls to handle dependencies

## Slide 98: Pipeline Stall for Data Hazards
ADD can read the updated register value from the register file in the same cycle as LW writes the loaded data to register
Do we really need to wait until LW updates the register file?
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11 | CC12 | CC13
LW | IF | ID | EXE | MEM | WB |  |  |  |  |  |  |  | 
ADD |  | IF | ID |  |  | EXE | MEM | WB |  |  |  |  | 
Next instr. |  |  | IF |  |  | ID | EXE | MEM | WB |  |  |  | 
Next+1 |  |  |  |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+2 |  |  |  |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+3 |  |  |  |  |  |  |  | IF | ID | EXE | MEM | WB | 
Next+4 |  |  |  |  |  |  |  |  | IF | ID | EXE | MEM | WB
nop
nop
nop
nop
Why don’t we use this data directly?

## Slide 99: Data Forwarding
Also known as “bypassing”
Take results still in the pipeline (not yet written back to a register) and pass them to dependent instructions
Forwarding Path
  Load instruction: from WB to EXE
  R-type instructions: from MEM to EXE

## Slide 100: Data Forwarding
Adder
ALU
Res.
Zero
D-Cache /
D-Mem
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Sum
+
A
B
S
4
0
1
ID/EX
EX/MEM
MEM/WB
0
1
IF/ID
Fetch Next instr.
00000060
0x10010004
$s0 = 0x10010000
$t1 = 0x0
$t4 = 0x24
$t5 = 0x0
Decode ADD
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
ADD $t5,$t1,$t4
$t1 reg. # / $s0 data / 0x04
Shift Left 2
Execute LW

## Slide 101: Data Forwarding
D-Cache /
D-Mem
Adder
ALU
Res.
Zero
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Sum
+
A
B
S
4
0
1
ID/EX
EX/MEM
MEM/WB
0
1
IF/ID
Fetch Next instr.
00000060
0x10010004
$s0 = 0x10010000
$t1 = 0x0
$t4 = 0x24
$t5 = 0x0
Decode ADD (stalled)
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
ADD $t5,$t1,$t4
Shift Left 2
Memory LW
NOP
$t1 reg #. / $s0 + 4
We still need a stall for LW to read data from memory

## Slide 102: Data Forwarding
D-Cache /
D-Mem
Adder
ALU
Res.
Zero
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Sum
+
A
B
S
4
0
1
ID/EX
EX/MEM
MEM/WB
0
1
IF/ID
Fetch Next instr. + 1
00000060
0x10010004
$s0 = 0x10010000
$t1 = 0x60
$t4 = 0x24
$t5 = 0x0
Decode Next instr.
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
Shift Left 2
Execute ADD
$t5 reg. # / 0x0 and 0x24
Next instr.
0x60
$t1 reg. # / 0x60
Writeback LW
NOP

## Slide 103: Data Forwarding
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11 | CC12 | CC14
LW | IF | ID | EXE | MEM | WB |  |  |  |  |  |  |  | 
ADD |  | IF | ID | ID | EXE | MEM | WB |  |  |  |  |  | 
Next instr. |  |  | IF | IF | ID | EXE | MEM | WB |  |  |  |  | 
Next+1 |  |  |  |  | IF | ID | EXE | MEM | WB |  |  |  | 
Next+2 |  |  |  |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+3 |  |  |  |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+4 |  |  |  |  |  |  |  | IF | ID | EXE | MEM | WB | 
Saved 1 cycles
compared to w/o forwarding
Only one stall to wait for LW reads data from memory
nop
nop

## Slide 104: Data Forwarding
As far as earlier instruction’s result is in pipeline, the result value can be forwarded to the following instructions
In arithmetic operations, no stall is needed
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
ADD | IF | ID | EXE | MEM | WB |  |  |  |  | 
SUB |  | IF | ID | EXE | MEM | WB |  |  |  | 
XOR |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+1 |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+2 |  |  |  |  | IF | ID | EXE | MEM | WB | 
Next+3 |  |  |  |  |  | IF | ID | EXE | MEM | WB
ADD $t3,$t1,$t2
SUB $t5,$t3,$t4
XOR $t7,$t5,$t3

## Slide 105: Forwarding Logic
Forwarding from MEM
  if (we_regM and (rsE ≠ 0) and (rf_waM = rsE)) ForwardAE = 10
  if (we_regM and (rtE ≠ 0) and (rf_waM = rtE)) ForwardBE = 10
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
ADD | IF | ID | EXE | MEM | WB |  |  |  |  | 
SUB |  | IF | ID | EXE | MEM | WB |  |  |  | 
XOR |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+1 |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+2 |  |  |  |  | IF | ID | EXE | MEM | WB | 
Next+3 |  |  |  |  |  | IF | ID | EXE | MEM | WB
ADD $t3,$t1,$t2
SUB $t5,$t3,$t4
XOR $t7,$t5,$t3
rsE & rtE
: source register id in EXE stage
rf_waM
: destination register id in MEM stage
we_regM
: register file write enable in MEM stage

## Slide 106: Forwarding Logic
Forwarding from WB
  if (we_regW and (rsE ≠ 0) and (rf_waW = rsE)) ForwardAE = 01
  if (we_regW and (rtE ≠ 0) and (rf_waW = rtE)) ForwardBE = 01
ADD $t3,$t1,$t2
SUB $t5,$t3,$t4
XOR $t7,$t5,$t3
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
ADD | IF | ID | EXE | MEM | WB |  |  |  |  | 
SUB |  | IF | ID | EXE | MEM | WB |  |  |  | 
XOR |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+1 |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+2 |  |  |  |  | IF | ID | EXE | MEM | WB | 
Next+3 |  |  |  |  |  | IF | ID | EXE | MEM | WB
rf_waW
: destination register id in WB stage
we_regW
: register file write enable in WB stage

## Slide 107: Forwarding Path
ALU
Res.
D-Cache /
D-Mem
Addr.
Read Data
Write Data
I-Cache / I-MEM
Addr.
Data
PC
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
IF/ID
0
1
EX
M
WB
Control
M
WB
WB
0
1
0
1
2
0
1
2
Forwarding Logic
20:16
15:11
rtE
rdE
rf_waE
25:21
MEM/WB
EX/MEM
rsE
ForwardBE
ForwardAE
rf_waM
rf_waW
Note: Logics for sign extensions and next pc calculation are omitted for simplicity
ID/EX

## Slide 108: Stall With Forwarding
For LW sourced dependency, we still need to stall for one cycle
  Freeze the PC and IF/ID pipeline register for one clock cycle
  Flush the ID/EXE pipeline register
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11 | CC12 | CC14
LW | IF | ID | EXE | MEM | WB |  |  |  |  |  |  |  | 
ADD |  | IF | ID | ID | EXE | MEM | WB |  |  |  |  |  | 
Next instr. |  |  | IF | IF | ID | EXE | MEM | WB |  |  |  |  | 
Next+1 |  |  |  |  | IF | ID | EXE | MEM | WB |  |  |  | 
Next+2 |  |  |  |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+3 |  |  |  |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+4 |  |  |  |  |  |  |  | IF | ID | EXE | MEM | WB | 
nop
nop

## Slide 109: Forwarding Path
ALU
Res.
D-Cache /
D-Mem
Addr.
Read Data
Write Data
I-Cache / I-MEM
Addr.
Data
PC
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
IF/ID
0
1
EX
M
WB
Control
M
WB
WB
0
1
0
1
2
0
1
2
Forwarding Logic
20:16
15:11
rtE
rdE
rf_waE
25:21
MEM/WB
EX/MEM
rsE
ForwardBE
ForwardAE
rf_waM
rf_waW
Note: Logics for sign extensions and next pc calculation are omitted for simplicity
Hazard detection unit
StallIF
en
StallID
FlushE
ID/EX

## Slide 110: Stalling Condition
Stalling Logic
  lwstall = ((rsD == rtE) or (rtD == rtE)) and dm2regE
  stallF = stallD = FlushE = lwstall
rsD & rtD
: source register id in ID stage
rtE
: destination register in EXE stage
dm2regE
: data memory to register write signal of the instruction in EXE stage

## Slide 111: Complete Datapath

## Slide 112: Pipeline Latency with Forwarding/Stall
Number of cycles we must stall to execute a dependent instruction:
Instruction that is the dependency source | w/o Forwarding (cycles) | w/ Forwarding (cycles)
LW | 2 | 1
Other instructions that update register file | 2 | 0
Data Hazards Solutions:
  - Hardware: stalling & forwarding
  - Software: compiler -- code reordering

## Slide 113: Code Scheduling to Avoid Stalls
Compiler can reorder code to avoid the stalls
C code for A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Find RAW dependencies and check if stall is needed

## Slide 114: Code Scheduling to Avoid Stalls
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
When forwarding is used,
only lw instruction causes stall
Leave lw instructions only
Compiler can reorder code to avoid the stalls
C code for A = B + E; C = B + F;
Find RAW dependencies and check if stall is needed

## Slide 115: Code Scheduling to Avoid Stalls
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Compiler can reorder code to avoid the stalls
C code for A = B + E; C = B + F;
Find RAW dependencies and check if stall is needed
lw instructions cause 1-cycle stalls
Leave instructions that are executed back-to-back only

## Slide 116: Code Scheduling to Avoid Stalls
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Now, check if the lw and dependent instructions must be executed back-to-back
Compiler can reorder code to avoid the stalls
C code for A = B + E; C = B + F;

## Slide 117: Code Scheduling to Avoid Stalls
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Compiler can reorder code to avoid the stalls
C code for A = B + E; C = B + F;

## Slide 118: Code Scheduling to Avoid Stalls
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
5 cycles for the first inst +
6 cycles for the remaining insts +
2 x 1 stall cycles = 13 cycles
Total
execution time
5 cycles for the first inst +
6 cycles for the remaining insts +
0 stall cycles = 11 cycles
Compiler can reorder code to avoid the stalls
C code for A = B + E; C = B + F;

## Slide 119: Control Hazard
Branch outcomes: Taken (T) or Not-Taken (NT)
Not known until late in the pipeline
  Prevents us from fetching future instructions
  Rather than stall, we can predict the outcome and keep fetching
  We only need to correct the pipeline if we guess wrong
Static Predictions
  Predict Taken
  Predict Not Taken
--- beq L1 L2 --- --- --- --- beq L2 L1 ---
T
T
NT
NT

## Slide 120: Statically Predict Not Taken
Keep fetching instructions from the PC + 4 by assuming that the branch will be not taken
Once branch is turned out to be taken, flush the incorrectly fetched instructions
In the following cycle, fetch the instruction from the branch target address

## Slide 121: Statically Predict Not Taken: Issues
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
Next instr. + 2
-- fetch
Next instr. + 1
-- decode
Next instr.
-- execute
BEQ -- If condition
satisfied, update PC
Next instr.
Next instr. + 1
Control / Displacement
Branch outcome only available in MEM stage
 Incorrect instructions already in pipeline

## Slide 122: Statically Predict Not Taken: Issues
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
Fetch from Branch Target Addr.
Flush
Flush
Flush
BEQ

## Slide 123: Static Branch Prediction Penalty
Penalty = number of instructions that need to be flushed on misprediction
For static branch prediction:
  The branch outcome and target address is available at the MEM stage and passed back to the Fetch stage
  If mispredicted, instructions of the correct path will be fetched on the next cycle
A 3-cycle branch penalty when mispredicted

## Slide 124: Statically Predict Not Taken
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM |  |  |  |  |  | 
ADD |  | IF | ID | EXE |  |  |  |  |  | 
SUB |  |  | IF | ID |  |  |  |  |  | 
OR |  |  |  | IF |  |  |  |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
NT!

## Slide 125: Statically Predict Not Taken
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM |  |  |  |  | 
SUB |  |  | IF | ID | EXE |  |  |  |  | 
OR |  |  |  | IF | ID |  |  |  |  | 
BNE |  |  |  |  | IF |  |  |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome

## Slide 126: Statically Predict Not Taken
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM |  |  |  | 
OR |  |  |  | IF | ID | EXE |  |  |  | 
BNE |  |  |  |  | IF | ID |  |  |  | 
AND |  |  |  |  |  | IF |  |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome

## Slide 127: Statically Predict Not Taken
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | EXE | MEM |  | 
AND |  |  |  |  |  | IF | ID | EXE |  | 
SW |  |  |  |  |  |  | IF | ID |  | 
LW |  |  |  |  |  |  |  | IF |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
T!
Flush

## Slide 128: Statically Predict Not Taken
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | EXE | MEM | WB | 
AND |  |  |  |  |  | IF | ID | EXE |  | 
SW |  |  |  |  |  |  | IF | ID |  | 
LW |  |  |  |  |  |  |  | IF |  | 
ADD |  |  |  |  |  |  |  |  | IF | ID
SUB |  |  |  |  |  |  |  |  |  | IF
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
nop
nop
nop
nop
nop
nop

## Slide 129: Predict Taken?
It is not possible to statically predict all the branches to be taken
  The branch target address is not computed until the EX stage, so we don’t have the PC values even needed to predict taken
Dynamic branch prediction + branch target buffer enables to predict taken
  Predict untaken a few times to collect branch target address of each branch and then predict taken based on the history
Can we reduce branch penalty with change of datapath?

## Slide 130: Early Branch Determination
Target address can be calculated earlier by moving shift-left-2 and Adder
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1

## Slide 131: Early Branch Determination
Target address can be calculated earlier by moving shift-left-2 and Adder
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
=
The comparison result is passed to control logic to take branch target address as next PC

## Slide 132: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM |  |  |  | 
OR |  |  |  | IF | ID | EXE |  |  |  | 
BNE |  |  |  |  | IF | ID |  |  |  | 
AND |  |  |  |  |  | IF |  |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
T!
Flush

## Slide 133: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | EXE | MEM | WB | 
AND |  |  |  |  |  | IF |  |  |  | 
ADD |  |  |  |  |  |  | IF | ID | EXE | MEM
SUB |  |  |  |  |  |  |  | IF | ID | EXE
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
nop
nop
T!
Flush
nop
nop

## Slide 134: Early Branch Determination: Issues
Target address can be calculated earlier by moving shift-left-2 and Adder
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
=
This may need extra data forwarding and stall
because now the operand value is needed in ID stage (not in EXE stage)

## Slide 135: Early Branch Determination
Forwarding logic for early branch determination
  ForwardAD = branchD and we_regM and (rsD ≠ 0) and (rf_waM == rsD)
  ForwardBD = branchD and we_regM and (rtD ≠ 0) and (rf_waM == rtD)

## Slide 136: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM |  |  |  | 
OR |  |  |  | IF | ID | EXE |  |  |  | 
BNE |  |  |  |  | IF | ID |  |  |  | 
AND |  |  |  |  |  | IF |  |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $s0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome

## Slide 137: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM |  |  | 
BNE |  |  |  |  | IF | ID | ID |  |  | 
AND |  |  |  |  |  | IF | IF |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $s0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
T!

## Slide 138: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | ID | EXE | MEM | WB
AND |  |  |  |  |  | IF | IF |  |  | 
ADD |  |  |  |  |  |  |  | IF | ID | EXE
SUB |  |  |  |  |  |  |  |  | IF | ID
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $s0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
nop
nop
nop
T!
If BNE has dependency with its preceding instruction, OR, one cycle stall is required to get the OR’s result value
 Still better than normal 3 cycle flushing

## Slide 139: Early Branch Determination
Stalling logic for early branch determination
  branchstall =
  branchD and we_regE and ((rf_waE == rsD) or (rf_waE == rtD))
  or
  branchD and dm2regM and ((rf_waM == rsD) or (rf_waM == rtD))
  StallF = StallD = FlushE = lwstall OR branchstall

## Slide 140: Branch Delay Slot
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | EXE | MEM | WB | 
AND |  |  |  |  |  | IF |  |  |  | 
ADD |  |  |  |  |  |  | IF | ID | EXE | MEM
SUB |  |  |  |  |  |  |  | IF | ID | EXE
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
nop
nop
T!
Flush
nop
nop
Find an instruction that
1) has to be executed regardless branch outcome
2) independent to branch
The instruction will be placed in the branch delay slot (right after branch instruction) instead of fetching wrong instruction and flushing

## Slide 141: Branch Delay Slot
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
BNE |  |  |  | IF | ID | EXE | MEM | WB |  | 
OR |  |  |  |  | IF | ID | EXE | MEM | WB | 
ADD |  |  |  |  |  | IF | ID | EXE | MEM | WB
SUB |  |  |  |  |  |  | IF | ID | EXE | MEM
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
BNE $a0,$s1,L2 (T)
OR $s0,$t6,$t7
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
No Flush
& Better Performance

## Slide 142: Branch Delay Slot
Branch delay slot is more useful for unconditional branches such as j, jal, jr because they are always taken
For example, if jal uses branch delay slot,
  After jal, $ra is updated with PC + 8
  The instruction in PC + 4 is executed after jal before entering the subfunction

## Slide 143: Dynamic Branch Prediction
Monitor the branch patterns for better prediction
  i.e. loops usually have a few iterations, so the branch in the loop is likely to be not taken at least for a few times
Branch Prediction Buffer (branch history buffer) is used to maintain each branch’s outcome history
  Small storage space indexed with certain bits of branch instruction’s PC value
  Each entry maintains the previous outcome of each branch
  Once the branch outcome is available, the corresponding entry is updated

## Slide 144: Branch Prediction Buffer
Aliasing issue
  Different branch instructions may map to the same branch prediction buffer entry if their PC values have the same LSBs, affecting each others’ predictions
    E.g., 0x8004 and 0x8104 will access the same entry if [3:2] bits are used for indexing
    Inevitable but can be alleviated with larger buffer
1000 0000 0000 0100
Branch instruction’s PC value (i.e. 0x8004)
[3:2] bits
 | prediction bit
0 | 1
1 | 0
2 | 1
3 | 1
Branch Prediction Buffer
The bits to be included to the prediction
may be different depending on the prediction buffer size
1: Predict Taken
0: Predict Not Taken
Prediction bit field can have multiple bits to record more history
 PC can be recorded to predict Taken

## Slide 145: 1-bit Predictor
Each entry of branch prediction buffer is 1-bit (1: Taken, 0: Not Taken)
  The entry value is the latest outcome of the branch
  Next outcome of the branch is predicted based on current value
  Example: Assume that the actual outcomes of the branches at 0xDC04, 0xDC08, and 0xDC20 are untaken, taken, and untaken, respectively
0xDC04 for(i=0;i<10000;i++)
{
0xDC08 if( ( i % 100) == 0 )
tick( );
0xDC20 if( (i % 2) == 0)
even();
}
prediction bit
0
1
0
..
predicted T
predicted NT
predicted NT
Actual result: NT
0
Actual result: NT
1
Actual result: T

## Slide 146: Is 1 bit Enough?
DC04: NNNNNNN ... NNNNNNNNNNT
10,000 iterations
Mis-predictions: 2 / 10,000
NT
TN
DC08: TTTTT ... TNTTTTT … TNTTTTT …
Mis-predictions: 2 / 100
DC20: TNTNTNTNTNTNTNTNTNTNTNTNTNTNT …
Mis-predictions: 2 / 2
Mis-predictions for every
first and last iterations
 99.998% Correct Prediction
98.0% Correct Prediction
0.0% Correct Prediction
10,000 iterations …
NNNNNNNNN …
Not taken and continue to the loop body
Taken to exit the loop

## Slide 147: Using 2-bit History
2-bit Saturating Counter in each branch prediction buffer entry
  Could have more than two bits but two bits cover most patterns (i.e. loops)
0
1
FSM for 1-bit
Prediction
00
01
10
11
FSM for 2-bit
Saturating Counter
Predict NT
Predict T
Transition on T outcome
Transition on NT outcome

## Slide 148: Example
2
T

3
T
3
T


…
3
N

N
1

T
0

0
T
1
T
T
T
T
…
T
1
1
1
1






T
1

T
…
1

0
T
1
T
2
T
3
T
3
T
…
3
T






Initial Training/Warm-up
1-bit
Predictor
2-bit
Predictor
Only 1 Misprediction per N branches now!
Correct prediction rates:
DC04: 99.999% , DC08: 99.0%, DC20: 50%

## Slide 149: Pipelined CPU Performance Analysis
Critical path = max {
Tpcq + Ti-mem + Tsetup,
2 ( TRFread + Tmux + Teq + TAND + Tmux + Tsetup ),
Tpcq + Tmux + Tmux + TALU + Tsetup,
Tpcq + Tmemread + Tsetup,
2 ( Tpcq + Tmux + TRFwrite )
}
Function Unit | Parameter | Delay (ps)
Register clock-to-Q | Tpcq | 30
Clock setup time | Tsetup | 20
MUX | TMUX | 25
Sign-extend | Ts_ext | 25
ALU | TALU | 200
Mem read | Tmem | 250
AND | TAND | 15
EQ | Teq | 40
Register file read | TRFread | 150
Register file write | TRFwrite | 20
RF write and read need to be finished in the first and second half of each cycle, respectively

## Slide 150: Pipelined CPU Performance Analysis
Critical path = 2 ( TRFread + Tmux + Teq + TAND + Tmux + Tsetup )
= 2 ( 150 + 25 + 40 + 15 + 25 + 20 ) = 550 ps
Function Unit | Parameter | Delay (ps)
Register clock-to-Q | Tpcq | 30
Clock setup time | Tsetup | 20
MUX | TMUX | 25
Sign-extend | Ts_ext | 25
ALU | TALU | 200
Mem read | Tmem | 250
AND | TAND | 15
EQ | Teq | 40
Register file read | TRFread | 150
Register file write | TRFwrite | 20